## Slide 1: Number Systems & Operations
Part I

## Slide 2: Decimal Numbers (Base 10)
People use decimal numbers.
I hope you know this very well. However, let’s review:


Ten digits  0-9
The value of a digit is determined by its position in the number.
. . . 102101100.10-110-210-3 . . .

## Slide 3: Binary Numbers
There are only 2 digits (0 and 1) and we can do binary counting as shown in the table.
Decimal
Binary
0
0
1
1
2
10
3
11
4
100
5
101
6
110
7
111
8
1000
9
1001
10
1010

## Slide 4: Binary Numbers (Base 2)
The weighting structure of binary numbers
2n-1 . . . 23 22 21
20.2-1 2-2 . . . 2-n
Positive power of two (whole number) |  |  |  |  |  | Negative power of two (fractional number) |  |  |  |  | 
25 | 24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6
32 | 16 | 8 | 4 | 2 | 1 | 1/2 | 1/4 | 1/8 | 1/16 1/32 1/64 |  | 
 |  |  |  |  |  | 0.5 | 0.25 | 0.125 | 0.0625 0.03125 0.015625 |  | 

## Slide 5: Binary-to-Decimal Conversion
Add the weights of all 1s in a binary number to get the decimal value.
ex: convert 11011012 to decimal
11011012 =
26
+
25
+
23
+
+
22 20
= | 64 + 32 + 8 + 4 | + 1
= | 109 | 
Weight | 26 | 25 | 24 | 23 | 22 | 21 | 20
bin | 1 | 1 | 0 | 1 | 1 | 0 | 1

## Slide 6: Binary-to-Decimal Conversion
Fractional binary example
ex: convert 0.1011 to decimal
0.1011 =
2-1
+
+
2-3 2-4
= | 0.5 + 0.125 + | 0.0625
= | 0.6875 | 
Weight | 2-1 | 2-2 | 2-3 | 24
bin | 1 | 0 | 1 | 1

## Slide 7: Decimal-to-Binary Conversion
Sum-of-weights method

To get the binary number for a given decimal number, find the binary weights that add up to the decimal number.
ex: convert 1210 , 2510 , 5810 , 8210 to binary
12 | = | 8+4 = 23+22 = 1100
25 | = | 16+8+1 = 24+23+20 = 11001
58 | = | 32+16+8+2 = 25+24+23+21 = 111010
82 | = | 64+16+2 = 26+24+21 = 1010010

## Slide 8: Decimal-to-Binary Conversion
Stop when the whole-number quotient is 0
Repeated division-by-2 method

To get the binary number for a given decimal number, divide the decimal number by 2 until the quotient is 0. Remainders form the binary number.
remainder |  |  |  | 
12/2 | = | 6 | 0 | LSB
6/2 | = | 3 | 0 | 
3/2 | = | 1 | 1 | 
1/2 | = | 0 | 1 | MSB
1210 = 11002

## Slide 9: Decimal-to-Binary Conversion
Converting decimal fractions to binary

Sum-of-weights
This method can be applied to fractional decimal numbers, as shown in the following example:
2-1+2-3
0.625 = 0.5+0.125 = = 0.101

Repeated multiplication by 2
Decimal fraction can be converted to binary by repeated multiplication by 2 (see details in the following slide.)

## Slide 10: Repeated Multiplication by 2 (by example) ex: convert the decimal fraction 0.3125 to binary
 |  |  |  |  | carry
0.3125 | x | 2 | = | 0.625 | 0
0.625 | x | 2 | = | 1.25 | 1
0.25 | x | 2 | = | 0.50 | 0
0.50 | x | 2 | = | 1.00 | 1
Continue to the desired number of decimal places or stop when the fractional part is all zero
MSB
LSB
0.312510 = 0.01012

## Slide 11: Binary Arithmetic
Basic of binary arithmetic




Binary addition
Binary subtraction Binary multiplication Binary division

## Slide 12: Binary Addition
The four basic rules for adding digits are as follows:




0+0=0  sum of 0 with a carry of 0
0+1=1  sum of 1 with a carry of 0 1+0=1  sum of 1 with a carry of 0 1+1=10  sum of 0 with a carry of 1

## Slide 13: Binary Addition (by example)
11 | 3 | 100 | 4
+11 | +3 | + 10 | +2
110 | 6 | 110 | 6
111 | 7
+ 11 | +3
1010 | 10
110 6
+100 +4
1010 10

## Slide 14: Binary Subtraction
The four basic rules for subtracting digits are as follows:
0-0 = 0
1-1 = 0
1-0 =
10-1 =
1
1 ; 0-1 with a borrow of 1

## Slide 15: Binary Subtraction (by example)
11 | 3 | 11 | 3
-01 | -1 | -10 | -2
10 | 2 | 01 | 1
101 | 5
-011 | -3
010 | 2

## Slide 16: Binary Multiplication
The four basic rules for multiplying digits are as follows:



0x0 = 0 0x1 = 0
1x0 = 0
1x1 = 1
Multiplication is performed with binary numbers in the same manner as with decimal numbers.
It involves forming partial products, shifting each successive partial product left one place, and then adding all the partial products.

## Slide 17: Binary Multiplication (by example)
11 | 3 | 101 | 5
x11 | x3 | x111 | x7
11 | 9 | 101 | 35
+11 |  | 101 | 
1001 |  | +101 | 
 |  | 100011 | 

## Slide 18: Binary Division
Division in binary follows the same procedure as division in decimal.
2
3 6
6
0
10
11 110
11
000
11
10 110
10
10
10
00
3
2 6
6
0

## Slide 19: 1’s and 2’s Complements
They are important since they permit the presentation of
negative numbers.
The method of 2’s complement arithmetic is commonly used in computers to handle negative numbers.

## Slide 20: Finding the 1’s complement
Very simple: change each bit in a number to get the 1’s complement
ex: find 1’s complement of 111001012
Binary
1’s complement
1 1 1 0 0 1 0 1
0 0 0 1 1 0 1 0

## Slide 21: Finding the 2’s Complement
An alternative method:

Start at the right with the LSB and write the bits as they are up to and including the first 1.
Take the 1’s complement of the remaining bits.
10110010 | 10111000 | binary
01001110 | 01001000 | 2’s comp
1’s complement
ex: 10110010  01001101  01001110
2’s complement
Add 1 to the 1’s complement to get the 2’s complement.
+1

## Slide 22: Signed Numbers
Digital systems, such as computer, must be able to handle both positive and negative numbers.
A signed binary number consists of both sign and
magnitude information.

The sign indicates whether a number is positive or negative.

The magnitude is the value of the number.

## Slide 23: Signed Numbers
There are 3 forms in which signed integer numbers can be represented in binary:



Sign-magnitude (least used)
1’s complement
2’s complement (most important)
Non-integer and very large or small numbers can be expressed in floating-point format.

## Slide 24: The Sign Bit
The left-most bit in a signed binary number is the sign bit.

It tells you whether the number is positive (sign bit = 0) or
negative (sign bit = 1).

## Slide 25: Sign-Magnitude Form
The left-most bit is the sign bit and the remaining bits are the magnitude bits.

The magnitude bits are in true binary for both positive and negative numbers.
ex: the decimal number +25 is expressed as an 8-bit signed binary number as:
00011001
While the decimal number -25 is expressed as
10011001

## Slide 26: Sign-Magnitude Form
“ In the
sign-magnitude
form, a negative
number has
the same magnitude
bits as the
corresponding positive
number but the
sign bit is a 1 rather than a 0. “

## Slide 27: 1’s Complement Form
Positive numbers in 1’s complement form are represented the same way as the positive sign-magnitude.
Negative numbers are the 1’s complements of the corresponding positive numbers.
ex: the decimal number +25 is expressed as:
00011001
While the decimal number -25 is expressed as
11100110

## Slide 28: 1’s Complement Form
“ In the
1’s complement
number is the 1’s
complement
form, a negative
of the
corresponding positive number. “

## Slide 29: 2’s Complement Form
Positive numbers in 2’s complement form are represented the same way as the positive sign-magnitude and 1’s complement form.
Negative numbers are the 2’s complements of the corresponding positive numbers.
ex: the decimal number +25 is expressed as:
00011001
While the decimal number -25 is expressed as
11100111

## Slide 30: 2’s Complement Form
“ In the
2’s complement
number is the 2’s
complement
form, a negative
of the
corresponding positive number. “

## Slide 31: Decimal Value of Signed Numbers
Sign-magnitude:

Both positive and negative numbers are determined by summing the weights in all the magnitude bit positions where these are 1s and ignoring those positions where there are 0s.

The sign is determined by examination of the sign bit.

## Slide 32: Decimal Value of Signed Numbers
Sign-magnitude (by example)
ex: decimal values of these numbers (expressed in sign-magnitude)
1) 10010101 |  | 2) 01110111 |  | 
1) 10010101 |  | 2) 01110111 |  | 
magnitude |  | magnitude |  | 
26 25 24 23 22 21 | 20 | 26 25 24 23 22 |  | 21 20
0 0 1 0 1 0 | 1 | 1 1 1 0 1 |  | 1 1
= 16+4+1 = 21 |  |  | = 64+32+16+4+2+1 = 119 | 
sign |  |  | sign | 
= 1  negative |  |  | = 0  positive | 
Hence: 10010101 = |  | -21 | Hence: 01110111 = 119 | 

## Slide 33: Decimal Value of Signed Numbers
1’s complement:

Positive – determined by summing the weights in all bit positions where there are 1s and ignoring those positions where there are 0s.

Negative – determined by assigning a negative value to the weight of the sign bit, summing all the weights where there are 1’s, and adding 1 to the result.

## Slide 34: Decimal Value of Signed Numbers
1’s complement (by example)
ex: decimal values of these numbers (expressed in 1’s complement)
1) 00010111
1) 00010111
2) 11101000
2) 11101000
-27
-27
26 25 24 23 22 21 20
0 0 0 1 0 1 1 1
26 25 24 23 22 21 20
1 1 1 0 1 0 0 0
= 16+4+2+1 = +23
= (-128)+64+32+8 = -24
Hence: 00010111 = +23
Hence: 11101000 = -23
+1

## Slide 35: Decimal Value of Signed Numbers
2’s complement:

Positive – determined by summing the weights in all bit positions where there are 1s and ignoring those positions where there are 0s.

Negative – the weight of the sign bit in a negative number is given a negative value.

## Slide 36: Decimal Value of Signed Numbers
2’s complement (by example)
ex: decimal values of these numbers (expressed in 2’s complement)
1) 01010110 2) 10101010
1) 01010110
2) 10101010
-27
-27
26 25 24 23 22 21 20
26 25 24 23 22 21 20
0 1 0 1 0 1 1 0
= 64+16+4+2 = +86
Hence: 01010110 = +86
1 0 1 0 1 0 1 0
= (-128)+32+8+2 = -86
Hence: 10101010 = -86

## Slide 37: Range of Signed Integer Numbers
The range of magnitude of a binary number depends on the number of bits (n).
Total combinations = 2n



8 bits = 256 different numbers
16 bits = 65,536 different numbers
32 bits = 4,294,967,296 different numbers

## Slide 38: Range of Signed Integer Numbers
For 2’s complement signed numbers:


Range = -(2n-1) to +(2n-1-1)
where there is one sign bit and n-1 magnitude
ex:
 |  | Negative Boundary | Positive Boundary
4 | bits | -(23) = -8 | (23-1) = +7
8 | bits | -(27) = -128 | (27-1) = +127
16 | bits | -(215) = -32,768 | (215-1) = +32767

## Slide 39: Floating-point numbers
How many bits do we need to represent very large number?
Floating-point number consists of two parts plus a sign.


Mantissa – represents the magnitude of the number.
Exponent – represents the number of places that the decimal point (or binary point) is to be moved.
Decimal number example: 241,506,800
Mantissa = 0.2415068
Exponent = 109
Can be written as FP as 0.2415068 x 109

## Slide 40: Binary FP Numbers
The format defined by ANSI/IEEE Standard 754-1985



Single-precision
Double-precision Extended-precision
Same basic formats except for the number of bits.



Single-precision = 32 bits
Double-precision = 64 bits
(Double) Extended-precision = 80 bits

## Slide 41: Single-Precision Floating-Point Binary Numbers
Standard format:



Sign bit (S) – 1 bit
Exponent (E) – 8 bits
Mantissa or fraction (F) – 23 bits
S(1)
E(8)
F(23)
Single-precision FP Binary Number Format

## Slide 42: Single-Precision Floating-Point Binary Numbers
Mantissa

The binary point is understood to be to the left of the 23 bits.

Effectively, there are 24 bits in the mantissa because in any binary number the left most bit is always 1. (say 001101100 is 1101100.)

Therefore, this 1 is understood to be there although it does not occupy an actual bit position.
S(1)
E(8)
F(23)
Single-precision FP Binary Number Format

## Slide 43: Single-Precision Floating-Point Binary Numbers
Exponent

The eight bits represent a biased exponent which is obtained by adding 127.

The purpose of the bias is to allow very large or very small numbers without requiring a separate sign bit for the exponents.

The biased exp allows a range of actual exp values from -126 (000000012) to +128 (111111102)
S(1)
E(8)
F(23)
Single-precision FP Binary Number Format

## Slide 44: Single-Precision Floating-Point Binary Numbers
Not easy, is it? Let’s see an example.
ex: 10110100100012 (assumption: positive number)
It can be expressed as 1 plus a fractional binary number.
Hence:
1011010010001 = 1.011010010001 x
212
The exponent,12, is expressed as a biased exponent as followed:
12+127 = 139 = 10001011
Therefore, we get:
0
10001011
01101001000100000000000

## Slide 45: Single-Precision Floating-Point Binary Numbers
Let’s do the opposite way:

To evaluate a binary number in FP format. General formula:
Number = (-1)S(1+F)(2E-127)
ex:
Number = (-1)(1.10001110001)(2145-127)
= (-1)(1.10001110001)(218)
= -11000111000100000002
1
10010001
10001110001000000000000

## Slide 46: Single-Precision Floating-Point Binary Numbers
Let’s review:

The exponent can be any number between -126 to
+128; that means extremely large and small numbers can be expressed.
Say, a 32-bit FP number can replace a binary integer number having 129 bits.
Distinctive point: Because the exponent determines the position of the binary point, numbers containing both integer and fractional parts can be represented.

## Slide 47: Single-Precision Floating-Point Binary Numbers
There are 2 exceptions to the format for FP numbers:
The number 0.0 is represented by all 0s.

Infinity is represented by all 1s in the exponent and all
0s in the mantissa.
x
00000000
00000000000000000000000
x
11111111
00000000000000000000000