## Slide 1: Number Systems & Operations
Part III

## Slide 2: Contents
1’s and 2’s Compliment
Signed Numbers
Decimal Value of Signed Numbers
Range of Signed Integer Numbers

## Slide 3: 1’s and 2’s Complements
They are important since they permit the presentation of negative numbers.
The method of 2’s complement arithmetic is commonly used in computers to handle negative numbers.

## Slide 4: Finding the 1’s complement
Very simple: change each bit in a number to get the 1’s complement
Example: find 1’s complement of 111001012
Binary | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
 | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓
1’s Complement | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0

## Slide 5: Finding the 2’s Complement
Add 1 to the 1’s complement to get the 2’s complement.
Example:
 |  |  | +1 | 
101100102 | → | 010011012 | → | 010011102

## Slide 6: Finding the 2’s Complement (Cont.)
An alternative method:
  Start at the right with the LSB and write the bits as they are up to and including the first 1.
  Take the 1’s complement of the remaining bits.
1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 |  | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 |  | binary
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 |  | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 |  | 2’s complement

## Slide 7: Contents
1’s and 2’s Compliment
Signed Numbers
Decimal Value of Signed Numbers
Range of Signed Integer Numbers

## Slide 8: Signed Numbers
Digital systems, such as computer, must be able to handle both positive and negative numbers.
A signed binary number consists of both sign and magnitude information.
  The sign indicates whether a number is positive or negative.
  The magnitude is the value of the number.

## Slide 9: Signed Numbers (Cont.)
There are 3 forms in which signed integer numbers can be represented in binary:
  Sign-magnitude (least used)
  1’s complement
  2’s complement (most important)
Non-integer and very large or small numbers can be expressed in floating-point format.

## Slide 10: The Sign Bit
The left-most bit in a signed binary number is the sign bit.
  It tells you whether the number is
    positive (sign bit = 0) or
    negative (sign bit = 1)

## Slide 11: Sign-Magnitude Form
The left-most bit is the sign bit and the remaining bits are the magnitude bits.
  The magnitude bits are same binary for both positive and negative numbers.
Example: the decimal number +25 is expressed as an 8-bit signed binary number as:
While the decimal number -25 is expressed as
Example: the decimal number +25 is expressed as an 8-bit signed binary number as:
While the decimal number -25 is expressed as

## Slide 12: Contents
1’s and 2’s Compliment
Signed Numbers
Decimal Value of Signed Numbers
Range of Signed Integer Numbers

## Slide 13: Contents
1’s and 2’s Compliment
Signed Numbers
Decimal Value of Signed Numbers
Range of Signed Integer Numbers

## Slide 14: End of Part II