## Slide 1: Number Systems & Operations
Part III

## Slide 2: Contents
1’s and 2’s Compliment
Signed Numbers
Decimal Value of Signed Numbers
Range of Signed Integer Numbers

## Slide 3: 1’s and 2’s Complements
They are important since they permit the presentation of
negative numbers.
The method of 2’s complement arithmetic is commonly used in computers to handle negative numbers.

## Slide 4: Finding the 1’s complement
Very simple: change each bit in a number to get the 1’s complement
ex: find 1’s complement of 111001012
Binary
1’s complement
1 1 1 0 0 1 0 1
0 0 0 1 1 0 1 0

## Slide 5: Finding the 2’s Complement
An alternative method:

Start at the right with the LSB and write the bits as they are up to and including the first 1.
Take the 1’s complement of the remaining bits.
10110010 | 10111000 | binary
01001110 | 01001000 | 2’s comp
1’s complement
ex: 10110010  01001101  01001110
2’s complement
Add 1 to the 1’s complement to get the 2’s complement.
+1

## Slide 6: Contents
1’s and 2’s Compliment
Signed Numbers
Decimal Value of Signed Numbers
Range of Signed Integer Numbers

## Slide 7: Signed Numbers
Digital systems, such as computer, must be able to handle both positive and negative numbers.
A signed binary number consists of both sign and
magnitude information.

The sign indicates whether a number is positive or negative.

The magnitude is the value of the number.

## Slide 8: Signed Numbers
There are 3 forms in which signed integer numbers can be represented in binary:



Sign-magnitude (least used)
1’s complement
2’s complement (most important)
Non-integer and very large or small numbers can be expressed in floating-point format.

## Slide 9: The Sign Bit
The left-most bit in a signed binary number is the sign bit.

It tells you whether the number is positive (sign bit = 0) or
negative (sign bit = 1).

## Slide 10: Sign-Magnitude Form
The left-most bit is the sign bit and the remaining bits are the magnitude bits.

The magnitude bits are same for both positive and negative numbers.
ex: the decimal number +25 is expressed as an 8-bit signed binary number as:
00011001
While the decimal number -25 is expressed as
10011001

## Slide 11: Sign-Magnitude Form
“ In the
sign-magnitude
form, a negative
number has
the same magnitude
bits as the
corresponding positive
number but the
sign bit is a 1 rather than a 0. “

## Slide 12: 1’s Complement Form
In this form, Positive numbers are represented the same way as the positive sign-magnitude.
Negative numbers are the 1’s complements of the corresponding positive numbers.
ex: the decimal number +25 is expressed as:
00011001
While the decimal number -25 is expressed as
11100110

## Slide 13: 1’s Complement Form
“ In the
1’s complement
number is the 1’s
complement
form, a negative
of the
corresponding positive number. “

## Slide 14: 2’s Complement Form
In this form, Positive numbers are represented the same way as the positive sign-magnitude and 1’s complement form.
Negative numbers are the 2’s complements of the corresponding positive numbers.
ex: the decimal number +25 is expressed as:
00011001
While the decimal number -25 is expressed as
11100111

## Slide 15: 2’s Complement Form
“ In the
2’s complement
number is the 2’s
complement
form, a negative
of the
corresponding positive number. “

## Slide 16: Contents
1’s and 2’s Compliment
Signed Numbers
Decimal Value of Signed Numbers
Range of Signed Integer Numbers

## Slide 17: Decimal Value of Signed Numbers
Sign-magnitude:

Both positive and negative numbers are determined by summing the weights in all the magnitude bit positions where these are 1s and ignoring those positions where there are 0s.

The sign is determined by examination of the sign bit.

## Slide 18: Decimal Value of Signed Numbers
Sign-magnitude (by example)
ex: decimal values of these numbers (expressed in sign-magnitude)
1) 10010101 |  | 2) 01110111 |  | 
1) 10010101 |  | 2) 01110111 |  | 
magnitude |  | magnitude |  | 
26 25 24 23 22 21 | 20 | 26 25 24 23 22 |  | 21 20
0 0 1 0 1 0 | 1 | 1 1 1 0 1 |  | 1 1
= 16+4+1 = 21 |  |  | = 64+32+16+4+2+1 = 119 | 
sign |  |  | sign | 
= 1  negative |  |  | = 0  positive | 
Hence: 10010101 = |  | -21 | Hence: 01110111 = 119 | 

## Slide 19: Decimal Value of Signed Numbers
1’s complement:

Positive – determined by summing the weights in all bit positions where there are 1s and ignoring those positions where there are 0s.

Negative – determined by assigning a negative value to the weight of the sign bit, summing all the weights where there are 1’s, and adding 1 to the result.

## Slide 20: Decimal Value of Signed Numbers
1’s complement (by example)
ex: decimal values of these numbers (expressed in 1’s complement)
1) 00010111
1) 00010111
2) 11101000
2) 11101000
-27
-27
26 25 24 23 22 21 20
0 0 0 1 0 1 1 1
26 25 24 23 22 21 20
1 1 1 0 1 0 0 0
= 16+4+2+1 = +23
= (-128)+64+32+8 = -24
Hence: 00010111 = +23
Hence: 11101000 = -23
+1

## Slide 21: Decimal Value of Signed Numbers
2’s complement:

Positive – determined by summing the weights in all bit positions where there are 1s and ignoring those positions where there are 0s.

Negative – the weight of the sign bit in a negative number is given a negative value.

## Slide 22: Decimal Value of Signed Numbers
2’s complement (by example)
ex: decimal values of these numbers (expressed in 2’s complement)
1) 01010110 2) 10101010
1) 01010110
2) 10101010
-27
-27
26 25 24 23 22 21 20
26 25 24 23 22 21 20
0 1 0 1 0 1 1 0
= 64+16+4+2 = +86
Hence: 01010110 = +86
1 0 1 0 1 0 1 0
= (-128)+32+8+2 = -86
Hence: 10101010 = -86

## Slide 23: Contents
1’s and 2’s Compliment
Signed Numbers
Decimal Value of Signed Numbers
Range of Signed Integer Numbers

## Slide 24: Range of Signed Integer Numbers
The range of magnitude of a binary number depends on the number of bits (n).
Total combinations = 2n



8 bits = 256 different numbers
16 bits = 65,536 different numbers
32 bits = 4,294,967,296 different numbers

## Slide 25: Range of Signed Integer Numbers
For 2’s complement signed numbers:


Range = -(2n-1) to +(2n-1-1)
where there is one sign bit and n-1 magnitude
ex:
 |  | Negative Boundary | Positive Boundary
4 | bits | -(23) = -8 | (23-1) = +7
8 | bits | -(27) = -128 | (27-1) = +127
16 | bits | -(215) = -32,768 | (215-1) = +32767

## Slide 26: End of Part III